BILCO Type LadderUP® Safety Posts provide easier, safer ladder access through roof hatches, floor access doors, and manholes. This telescoping post permanently mounts to the top two rungs of any fixed ladder, providing a positive hand-hold and enabling the user to enter or exit an opening in an upright and balanced position. For more information, please visit our website www.bilco.com or call 1-800-366-6530.

SECTION 077233

ROOF HATCHES

(BILCO TYPE LU)

GENERAL

SUMMARY

Work Included:  Provide factory-fabricated ladder safety posts.

SUBMITTALS

Product Data:  Submit manufacturer’s product data.

Shop Drawings: Submit shop drawings including profiles, accessories, location, adjacent construction interface, and dimensions.

Warranty:  Submit executed copy of manufacturer’s standard warranty.

QUALITY ASSURANCE

Manufacturer:  A minimum of 5 years experience manufacturing similar products.

Installer:  A minimum of 2 years experience installing similar products.

Manufacturer’s Quality System: Registered to ISO 9001 Quality Standards including in-house engineering for product design activities.

DELIVERY, STORAGE AND HANDLING

Deliver products in manufacturer’s original packaging.  Store materials in a dry, protected, well-vented area. Inspect product upon receipt and report damaged material immediately to delivering carrier and note such damage on the carrier’s freight bill of lading.

WARRANTY

Manufacturer’s Warranty:  Provide manufacturer’s standard warranty.  Materials shall be free of defects in material and workmanship for a period of five years from the date of purchase. Should a part fail to function in normal use within this period, manufacturer shall furnish a new part at no charge.

PRODUCTS

MANUFACTURER

Basis-of-Design Manufacturer:  Type LU Ladder Safety Post by The BILCO Company, P.O. Box 1203, New Haven, CT 06505, 1-800-366-6530, Fax: 1-203-535-1582, Web: www.bilco.com.  Comply with the following:

LADDER SAFETY POST

Furnish and install where indicated on plans ladder safety post Model [insert LU-1, LU-2, LU-3, or LU-4].  The ladder safety post shall be pre-assembled from the manufacturer.

Performance characteristics:

Tubular post shall lock automatically when fully extended.

Safety post shall have controlled upward and downward movement.

Release lever shall disengage the post to allow it to be returned to its lowered position.

Post shall have adjustable mounting brackets to fit ladder rung spacing up to 14” (356mm) on center and clamp brackets to accommodate ladder rungs up to 1-3/4” (44mm) in diameter.

Post: Shall be manufactured of high strength square tubing. A pull up loop shall be provided at the upper end of the post to facilitate raising the post.

Material of construction: Shall be [insert: steel (Model LU-1, LU-2); or Type 304 stainless steel (Model LU-3); or aluminum (Model LU-4)].

Balancing spring: A stainless steel spring balancing mechanism shall be provided to provide smooth, easy, controlled operation when raising and lowering the safety post. [For installation in highly corrosive atmospheres, Model LU-3 incorporates a special alloy spring mechanism].

Hardware: All mounting hardware shall be Type 316 stainless steel.

Finishes: Factory finish shall be [insert: yellow powder coat steel (Model LU-1); or hot dip galvanized steel (Model LU-2); or mill finish stainless steel (Model LU-3); or mill finish aluminum (LU-4)].

EXECUTION

EXAMINATION

Examine substrates and openings for compliance with requirements for installation tolerances and other conditions affecting performance.  Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.  Locate units level, plumb, and in proper alignment with adjacent work.

Test units for proper function and adjust until proper operation is achieved.

Repair finishes damaged during installation.

Restore finishes so no evidence remains of corrective work.

ADJUSTING AND CLEANING

Clean exposed surfaces using methods acceptable to the manufacturer which will not damage finish.

END OF SECTION